Neuralink Interview Task
Report

FAULHABER Client

Task owner:Murat Terzi

Date: February 5th, 2018

Contents

1 Summary	#3

2 Client Details	#4,5

3 Low level Details	#6

4 Debugging Tool Details	#7

5 Discussion	#8

1)Summary

Goal is to implement tools for controlling Faulhaber motor over RS-232. Manual for motion controller is provided by Neuralink. In this task, eight commands were used and the commands are:

ANSW2 - All commands with confirmation and asynchronous responses
NP – notify when position attained
OST – operation status
M - move
GN -get current velocity
POS – get current position
LA -load absolute position
GOHOSEQ – run home sequence

Low level is written in C. high level and debug tool are written C++.

2)Client Details
Client supports synchronous and asynchronous operations. It has six operations and two functions.
Important note: if detailed messages wanted, uncomment #define FULL_INFO in faulhaber_highlevel.h file
Operations
a) DefaultValues
Since motion controller wasn’t available, there was no way to check default values. Even though manual explains some of the default values, I wanted to set ANSW2 and NP for complete synchronous communication. This operation sets these values and return.
NOTE: I assumed that ANSW2 responses OK.

b) StartHoming
This operation creates a command called GOHOSEQ and sends it to the controller. It successfully returns if it receives OK.

c) StartMoveTo
This operation creates two commands called LA# and M then it sends it to the controller. It successfully returns if it receives two OKs.

d) GetState
This operation starts creating a pointer(state) and fills it with NULLs. Then sends POS, GN and OST in order. Then it fills this pointer with returned values if it receives OK. POS command gets the current position where GN gets the current velocity. Homed iss set to true if position is 0. OST is a unique command, it sends back 18 bit message. 16th bit is used or updating ‘moving’ state.

e) Home
This is a synchronous operation. It does not return until receives ‘p’. Comamnd is set to GOHOSEQ.

f) MoveTo
This is the second synchronous operation. First it loads the target position by sending LA# then continues if it receives OK. Next, it sends the M command. It successfully returns if it receives ‘p’.

Functions
b) ASync_operation
This uses low level functions to create a mid-level function. It takes, fd, serialport, baudrate, command, acknowledgment response, end of character, success message, timeout and optional argument for special commands that need argument.
For Example:
Async_operation(fd, /dev/ttyACM1, 9600, “LA”, “OK”, “\n”, “Load-position completed”, 6500, 5000)
-it creates and opens /dev/ttyACM1 with 9600bs.
-Sends LA5000 command, starts count down, starting at 6500msec.
-if it receives OK\n, then it returns 1 and outputs success message
-if time is out , it returns -2(timeout)
-if fails, it returns -1(fail)

a) Sync_operation //this can be updated with two timeouts
This function is like Async_operation. In addtion to that, it also saves the response and it comes with optional expected repose to check if operation completed after acknowledgment received.
For example :
Sync_operation(fd, /dev/ttyACM1, 9600, “M”, “OK”, “\n”, “Move completed”, 6500, char response, “p”)
-it creates and opens /dev/ttyACM1 with 9600bs.
-Sends M command, starts count down, starting at 6500msec.
-if it receives OK\n, then outputs message(#define FULL_INFO ) and continues
-if time is out , it returns -2(timeout)
-if fails, it returns -1(fail)
-New count down, starting at 6500msec.
-if it receives p\n, then outputs move completed and returns 1
-if time is out , it returns -2(timeout)
-if fails, it returns -1(fail)

3)Low Level Details

Low level code can be seen in faulhaber_low_level_SerialPort.c. There are five functions.
Important note: if read_debugging wanted, uncomment #define DEBUG faulhaber_low_level_SerialPort.c file

a) serialport_setup
This is the main function that creates the fd. It sets the flags and opens the port. It returns with POSIX messages.
b) serialport_flush
This function flushes the fd so new data can be read.
c) serialport_close
This function closes the fd.
d) serialport_write
This function writes data to serial.
e) serialport_read_until
Task required a timeout and end of character for reads. Therefore this function created to look for an end of character and return or if time is out it returns timeout error.

4) Debugging Tool Details

Usage: [OPTIONS] -c <Commands>

Options
-b, --baudrate (default:9600)
-s, --serialport (default:/dev/ttyS0)
-p, --position (default:0 mm)
-a --async_timeout=ms (default:5000ms)
-t --sync_timeout=ms (default:60000ms)

Required:
   -c --Commands

Commands:
    getstate	-print current Homed, Moving, Velocity, Position
    moveto	- sync move to position (if no -p entered, default:0 mm)
    home	- sync homing
    starthoming	- async homing
    startmoveto	- async move to position (if no -p entered, default:0 mm)
    defaultvalues	-load default values.(set ANSW2 and NP)

ORDER IS IMPORTANT FOLLOW THIS:
-b [baudrate] -s [serialport] -p [position] -a [async_timeout] -t [sync_timeout] -c <command>

Example: (sync-moveto 50mm, port at /dev/ttyACM1 with default baudrate)

./run faulhaber -s /dev/ttyACM1 -p 50 -c moveto

5) Discussion

Having different types(sync or asyn) of operations might confuse people once you have 10+ operations. It still depends on the usage and it is open to discussion that if less operations are better or not. However in my opinion we can ignore syn and asyn operations and create one operation type that uses Linux poll (which can be async communcation, multiplexed comm, etc). By using that programmer can decide blocking or non blocking client. But if the usage for client also includes other things rather than just motor controlling than I would keep the asyn and sync operations.
I would create one function that uses poll.h and waits for the completion(for example ‘p’ response) in another thread. Whenever that thread informs us that there is data coming, getstate can join to that thread and it can read the data automatically. Even though it helps, we might also lose reponse data.
For this task, I assumed programmer wants to kick moving or homing and do work. Then, he/she checks states whenever wanted. I didn’t use the poll.h and a thread in this case because getstate will still block the port or might confuse the motion controller by sending too many commands which manual warns us about. Getting multiple values from multiple nodes will mess up the asynchronous communication.
Overall, this faulhaber client that I created, can communicate with the motion controller, execute commands and receive responses with or without blocking the client.
I also want to add that I would rather to do test driven development with an actual motion controller.